## Slide 1: Pressure Tank

## Slide 3
Ⅰ.What are the types of pressure tanks currently used by our company?
Divided by colour:LEO colour-ODM,other customizable colour-OEM.
24 V T T S G1 S
Stainless steel cover S
(Plastic cover P, Iron cover can be omitted.)
Cover thread
Stainless steel tank S (Iron can be omitted)
Actual Capacity=Nominal Capacity
Pressure tank
Tank type: V-vertical pressure tank ,
(C-horizontal pressure tank, S-vertical flat pressure tank,
F-Vertical pressure tank with foot)
Normial Tank Capacity

## Slide 4
Ⅰ.What are the types of pressure tanks currently used by our company?
P.S:EPDM:A kind of synthetic material resistant to oxidation and corrosion.
NR: A natural rubber with good elasticity, high strength and comprehensive performance.
Butyl: Good stability, excellent air tightness and water tightness.

## Slide 5
Ⅰ.What are the types of pressure tanks currently used by our company?

## Slide 7
ⅠQ:What are the functions of the pressure tank?
A:1.Keep water pressure stable.
2.During the working cycle of the pressure switch,prevent the micro- leakage of the pipeline or use a small amount of water from causing the pump to start frequently and affect the life of the pump.
3.Storage water.
4.Extend pump life.
Tank body
Airbag
Intake valve
Dust cover
Pressure
tank cap
Connector
Air pressure chamber
水箱
Tank
Filter

## Slide 8
Ⅱ.What is the internal working principle of the pressure tank?
Water
Air
bag
Compressed air
Water storage area
Comp-ressed air

## Slide 9
The water pressure decreased in pipeline
When air pressure > water pressure
water entering the airbag from pipeline
The air expand and
the pressure drop
when water pressure=Pressure switch on value
Tap on
Pressure switch on
Pump start
Water stop coming out from airbag
Ⅲ.Working process

## Slide 10
The water pressure increased in pipeline
When water pressure>air pressure
water entering the airbag from pipeline
The gas is compressed and
the pressure raise
when water pressure=Pressure switch off value
Water sotp entering airbag
Tap off
Pressure switch off
Pump stop

## Slide 11
Tap
Pressure switch
Pressure tank
ON
OFF
OFF
OFF
OFF
ON
FULL
FULL
OUT
IN
EMPTY
Ⅳ.State diagram

## Slide 12
Ⅴ.The difference between pressure tank system and electrinical switch
Switch on:
P:Water pressure < Set switch on pressure
E:Water pressure < Set switch on pressure + Flow
Function:
P:Automatic start-stop+Steady pressure+Storage water+Extand pump's life
E:Automatic start-stop+Dry-run protection

## Slide 14
Ⅳ.Q:Where are the different types of pressure tanks used and how they are installed?
CT-
Horizontal
pressure tank
VT-
Vertical
pressure tank
ST-
Vertical flat
pressure tank
FT-
Vertical pressure
tank with foot

## Slide 15
Ⅷ.How to select the right pressure tank?
V=K×Amax×（Pmax×Pmin）/[(Pmax－Pmin)×Ppro]
V:Pressure tank volume Amax：Maximum pump flow
K:Pump operating coefficient
Pmax:Pipe water pressure when the switch is off
Pmin:Pipe water pressure when the switch is on
Ppro:Pressure tank preflush pressure
The value of K at different power pumps |  |  |  |  | 
P(HP) | 1-2 | 2-4 | 5-8 | 9-12 | >12
K | 0.25 | 0.375 | 0.625 | 0.875 | 1
1HP=0.75KW
Sugggestion：

## Slide 17
Ⅰ.What are the key parts of the pressure tank? How long is its life?
What are the factors that affect life?
Key parts：Airbag, valve core, tank body
Life：The garden pump has a regular durability of 2500h (24h continuous operation).
Factors:
1,Corrosive media may corrode airbags
2,The aging of the airbag
3,The wear between the airbag and the tank
4,There may be burrs on the inner wall of the tank to damage the airbag

## Slide 18
Ⅱ.How does the pressure tank inflate? What are the points of attention?
If the air pressure is insufficient, we will use the device to inflate and test.
Equipment: compressed air inflatable gun,pressure gauge
Attention:1.Refer to the pressure gauge to ensure accurate air filling.
2.Do not damage the valve core.

## Slide 19
TIP:
1.In LEO, most of the preflush pressure value is equal to the starting value of the pressure switch,about 1.6bar.
Tank body:Iron
2.Standard configuration: Plastic pump:PA6-GF25
Tank cap
Others:ST12
P.S:Stainless steel material is available on request.
3.Generally speaking, the tank body engraved with Leo logo, unless the customer has a request.
4.It is not recommended that customers replace air bags by themselves.On the one hand, the sealing of gas tank cannot be guaranteed;On the other hand, the replacement cost is too high.